::::::::::::::::::::::::::::::::::::::::::::::::::::::::::::::::::::::::::::

DISK.DOC
---------




This diskette should contain 6 additional files:

     CONTROLR.DEF	 The "master" .DEF file for the Am29116
			+ misc other parts in comma-positional
			 notation.

     CONTROLR.SRC	 A test SRC file (partial microword).

     DISKCTLR.DEF	 The .DEF file for the Am29116-Am9520
			 (BEP) based disk controller that is
			 discussed in the application note,
			 "A High Performance Intelligent Disk
			 Controller" by O. Tabler and B. Kitson.
			 This file is in DEF statement-overlay
			 format.

     DISKCTLR.SRC	 The source code for the isk controller.
			 (This file assembles to a 92K P2L file.)

     Am29CPU.DEF	 The "MASTER" .DEF file for RALU-based
			 designs (Am2901-2903 or 29203) RALUs
			 + misc other parts in comma-positional
			 notation.

     Am29203.SRC	 Sample source code for an Am29203 CPU
			 (Am2910 sequencer). (Uses Am29CPU.DEF)


These  AMDASM.DEF  files  are provided as a  service  to  AmSYS29
customers.   They  are intended to provide a basis from which the
customer   may	selecthose  equates,   subs  and   definitions
appropriate to a given design problem.	 It is intended that  the
customer  edit	a copy of one or more .DEF files to  produce  the
desired .DEF file.

The  .SRC files are provided as a reference.   The microword will
probably not match the customer's requirements.



CONTROLR.DEF
-------------


Originally created as a master file for study, it has been edited
into one application, "DISKCTLR.DEF".   It is recommended that the
user   compare	 these	two  .DEF  files  for  similarities   and
differences.

The  file includes a number of parts which may or may not  appear
in  a  controller.   The first page after  the	WORD  declaration
provides an effective index to the file.   The various EQU groups
of the Am29116 instructions are indexed ([i]) for cross reference
by  the  DEF statements.   Each instruction type has its own  DEF
statement.

The  Am2910 instructions,  without any of the additional  control
lines (OEy,  RLD,  CCEN) are presented with a SUB statement.  The
Am2910,  a  3-bit  conditional MUX field,  and a 12-bit  variable
address  field are part of each of the following DEF  statements.
By editing the SUB statement, all of the other DEF statements can
be altered.

This means that any of the three fields can be altered or  even
eliminated by editing one statement.


Control_lines

Several  of the control lines for the Am29116 are presented in	a
second	SUB statement.	 Note that not all of the  Am29116  lines
appear (the Ti lines, for example, were not input).

This  manner of definition requires comma positional substitution
in  the  source  file.	 These	lines  can  be	edited	into  DEF
statements  and  the  SUB deleted to  convert  the  control  line
specification  to  overlays.   The  required usage  and rsonal
preference are the deciding factors in the approach.


Instructions

Pages 8-20 are the Am29116 instructions.   Each class is  defined
by first defining the mnemonics and then the DEF statement.   The
mnemonics  are taken directly from the Am29116 data  sheet.   For
example,  SOR,	the single operand-RAM instruction format (page 5
of  the Am29116 data sheet) has a choice of word-byte mode ([m]),
1  of 4 op codes ([1]),  1 of 10 source-destination pair  selects
([2]), and requires a RAM register address ([R]).


Am2914

The instruction set only is defined.

Am2940

The  instruction  set only is defined.	 The instruction  set  is
flagged by ".40" to avoid duplicate mnemonics with the Am2942.


Am2942

The instruction set only is defined.


Am2904

The Am2904 instruction set is very powerful and extensive.   Some
ideas for mnemonics are given for shift control and various other
commands and  some sample DEF statements are included.

The user must define the Am2904 by defining only what is required
for a given design.  There are no standard mnemonics.


Am2925

Equates  for  cycle length codes plus  place-holders  (incomplete
definition)  for control lines are provided.   Again,  DEF state
ments may be used instead.


Am2950/51

A comment only.


CONTROLR.SRC
------------


This source file is for debug of the preceding .DEF file.  It was
prepared primarily for study.

Page  3 provides calls to the single operand instructions.   SONR
requires  an  immediate data word and it is provided via  a  free
format (FF) statement.


Example:

  SOR	,,, W, MOVE, SORA, R10

  SONR	,,, W, MOVE, SOI, NRS
  FF	H#E, 15X, H#0123, B#01000, 24X



Note the commas.  This can be avoided by the use of overlays.

(Note that this is an incomplete microword.)



CONTROLR.DEF_+CONTROLR.SRC_MICROWORD


     2910      COND	  BR	   29116
     INSTR     MUX	 ADDR	   CTLs      OPEN

       4	3	  12	    16	      24    =	64 bits


Note  on  address  fields:   To avoid  problems,  use  $  as  the
attribute in address field for AMDASM, i.e.12V$X, 6V$X, etc.


Note  on microword:   This incomplete microword was laid out  for
study  of  the Am29116 and will not necessarily match  an  actual
microword  format for a controller.   The 24 don't cares would be
replaced by other controls and the microword might be larger than
64 bits.



DISKCTLR.DEF
------------






An  AMD application note is being prepared which discusses a high
performance  disk controller.	The .DEF file for the  controller
was created by editing the "master" file.

The  Am29116 instructions were left basically intact;  the  major
change	was the deletion of the Am2910 and ZZZZZ SUB  statements.
The  length  of the microword was also increased from  64  to  80
bits.	A  global  substitution (under ED,  the editor)  replaced
Am2910 by nothing and ZZZZZ by 64X.

The instruction sets for all other parts were deleted.	Beginning
on  page  19,  EQUs and DEFs were added according to  the  design
requirements.	The choice here was to use overlay in the  source
file;  therefore,  all	Am2910	instructions were defined as  DEF
statements rather than equates.


Immediate_Operand

The  study  file used FF statements in the .SRC file  to  provide
data for immediate data operand instructions.	Here,  IMME is	a
DEF statement which can be overlayed with other DEF statements to
build a microword.


Control_Lines

Control  lines for the Am29116 are defined in DEF statements  for
overlay.


Am2910

The  Am2910 command are defined in DEF statements.   Note the use
of JS,	JP, RTN, IF and IF NOT which have been added to the basic
16 instructions.


Misc_Control_Signals

All of the remaining control signals appear as DEF statements for
overlay in the source file.





     The_Microword_-_DISKCTLR.DEF


     Bit_Position________#_________Function_________________

	0-15		16	   Am29116 Instruction

	0-15		16	   Immediate Data Operand

       16-19		 4	   CT Multiplexer Control (Ti Lines)

	20		 1	   Status Register Enable

	21		 1	   Ouput Enable - Yi

	22		 1	   Instruction Enable

	23		 1	   Data Latch (D-I-Latch) Enable

       24-27		 4	   Am2910 Instruction

       28-37		10	   Branch Address

       38-42		 5	   Condtion Code Selections

	43		 1	   Parity

	44		 1	   Address Mark Control

	45		 1	   Memory Bus from Drive Control Bus

	46		 1	   Memory Bus from Translate PROM

	47		 1	   Memory Bus from 9403AS

	48		 1	   Memory Bus from Am29116

	49		 1	   Memory Bus from Am9520 - LSB

	50		 1	   Memory Bus from Am9520 - MSB

	51		 1	   (Disk) Bus Direction out from
				  Controller

	52		 1	   Memory Bus to 9403AS

	53		 1	   Memory Bus to Am29116

	54		 1	   Memory Bus to Am9520 - LSB

	55		 1	   Memory Bus to Am9520 - MSB




     Bit_Position________#_________Function______________________

	56		 1	   Memory Bus to Am9520 - Control
				   Information

	57		 1	   Clock Enable Am9520 to Lower-
				   Byte Bus Int.

	58		 1	   Clock Enable Memory Bus to
				Am9520 Transfer

	59		 1	   Clock Pulse (Actual Waveform)
				   for Am9520

	60		 1	   Command Request

	61		 1	   Input Serial Data to 9403AS

      62-63		 2	   Jump Indirect Am29116 Register

      62-63		 2	   No Indirect Jump

	64		 1	   Memory Access

	65		 1	   Memory Address

	66		 1	   Memory Write

	67		 1	  Output Serial Data from 9403AS

	68		 1	   Parameter Enable

	69		 1	   Set 9520 P Bits from 9520 PM Bits

	70		 1	   Parallel Fetch from 9403AS

	71		 1	   Parallel Load into 9403AS

	72		 1	   Parameter Request

	73		 1	   Read Gate

	74		 1	   Reset FIFO

	75		 1	   Select/Attention Strobe

	76		 1	   Write Gate

      77-79		 3	   Translate Prefix







Example_Source_Code_Lines


     SOR  W, MOVE, SORY, R4  & NODLE  & NOIEN
\    & OEY  & NOSRE  & MADR  & NOJMPI  & CONT
;    MOVE R4 TO MAR


     SOR  W, MOVE, SOZR, R0  & NODLE  & IEN
\    & NOOEY  & NOSRE  & NOJMPI  & RTN
;    Load 0 into R0 and return





    DISKCTLR.SRC
    --------------



This file, a very large one, was prepared for the AMD application
note,  "A High Performance Disk Controller".  The code is written
using  overlaid  DEF  statements  with	positional  substitutions
minimized (primarily appears in the Am29116  instructions).   The
code is commented.


Am29CPU.DEF
-------------


The   original	 AmSYS29  software  included  a   library   file,
AM2900.LIB,  which  provided the user with a source of predefined
mnemonics for various parts.   The AM29CPU.DEF file is the latest
descendant of that original file.

The  AM29CPU.DEF  file provides mnemonics for a number	of  parts
considered to be likely to appear in a CPU design,  as opposed to
a  controller  design.	 This includes	the  Am2901,  Am2903  and
Am29203  RALUs.    Flags  are  used  to  differentiate	duplicate
mnemonics.  (The Am29203 is given priority.)

The user must edit a version of this file to complete a .DEF file
for  a	particular application.   Most of the equate  groups  are
indexed ([i]) for cross reference from DEF and SUB statements.




Am2901
  The oldest RALU, the function and destination fields are flagged, by .01.
Example  SUB statements are included  following  the   equates.
The mnemonics are from the data sheet.

Am2914

Only the instruction set is included

Am2930

Only the instruction set is included

Am2932

Only  the  instruction set is included.   The instruction set  is
flagged by ".32" to differentiate it from that of the Am2930.


Am2940

Only the instruction set is included.







Am2902_-_Am29203

The  instruction  set  is  flagged by ".03"  in cases  where  it
duplicates  that of the Am29203.   Certain equate groups  (source
select	and  destination for example) are the same  for  the  two
parts.	 The  differences are in the function set and the special
functions.   While many of the equates in these actually were the
same,  there  were  enough  differences  to  flag  that  separate
definitions were felt to be clearer.


Expanded_Memory

The Am2903 and Am29203 have expandable registers.   The  Am29705/
29707  2-port memories allow groups of 16 registers to be  added.
This changes the microword source fields.   Examplnemonics are
provided for a particular diagram.


Register [R]

All RALUs use 4-bit addresses for the on-board registers.


Carry

A  few	not-inclusive  definitions are	provided.   This  is  not
programming for the Am2904.


Am2910_-_Am29811

The  instruction  set for the Am2910 is  provided.   The  Am29811
differs only in the last mnemonic,  substituting JP for TWB.   An
example SUB statement is provided.


Am2925

Cycle  length  codes  and  an indication  of  control  lines  are
provided.  The control line definitions are incomplete.


Am2904

As  in te CONTROLR.DEF file -- incomplete as far as total Am2904
capabilities.	Intended  to provide ideas.   The  customer  must
create his or her own definitions for equates and DEF statements.
There are no standard mnemonics.






DEF_Statements

Comma  positional within the part and overlay are used to  create
the  microword.   The DEF statements are intended to  demonstrate
typical ALU and sequencer definitions.	The balance of the micro
word is undefined.

Note  the use of commented default line plus the index	reference
[i].   The  reference  identifies equate mnemonics which  may  be
substituted  in  a given varible field in place of  the  default
value.

DEF  statements  for the Am2904 are given as well  as  statements
specific   to  a  particular  .SRC  file.    This  was	done  for
demonstration -- one DEF file may be used with more than one  SRC
file.	The  .DEF  file  is  then the  main  or  master  mnemonic
reference for a set of source programs.




Am29203.SRC


This  file,  developed from one that was originally prepared  for
the  Am2903  (AM2903.SRC)  was	prepared to  demonstrate  how  to
program the Am29203.

The microword is in a conceptual, standard format:


   2 9 1 0	     2	   9	 2    0   3		      2 9 0 4
2910  COND  BR	SOURCE	FUNC  DEST  CARRY  Ra	Rd  Ien  0ey   Shift  SE
INSTR MUX  ADDR    A	  L	U     IN  ADDR ADDR	  en   INSTR  en
  4    3    12	   3	  4	4     2    4	4    1	  1 14x  4    1 3x

		  47 bits + 17 don't cares = 64 bit word



Sample_Code_Lines

AM2910	RPCT,  ,LB & AM29203  ,SPECL, MULT, NOCARRY, R1, R0

AM2910	& AM29202  RAMAB,  ,RAM,,,R15,,OENDIS

AM2910	& AM29203  ,ADD,RAMQUPA,NOCARRY,R2,R2  & SHIFT SUR2Q2


Since the code was prepared for study,	it is more detailed  than
might  otherwise be necessary;	i.e.,  defaults are resubstituted
occasionally, etc.  Improvements in readability could be obtained
by  the  use of specialized DEF statements and increased  use  of
overlays.