UIOFRST   UIOF Format Reset Utility
       Copyright Summagraphics Corporation 1991.  All Rights Reserved.

UIOFRST transmits a reset command (<ESC> Z) to the tablet out the
selected serial port.

Usage:  UIOFRST [options]
        /1	  selects serial port 1 (PC, XT, AT, PS/2)
	/2	  selects serial port 2 (PC, XT, AT, PS/2)
	/3	  selects serial port 3 (PS/2 only)
	/4	  selects serial port 4 (PS/2 only)
	/5	  selects serial port 5 (PS/2 only)
	/6	  selects serial port 6 (PS/2 only)
	/7	  selects serial port 7 (PS/2 only)
	/8	  selects serial port 8 (PS/2 only)
	/BAxxxx	  selects serial port with base address of xxxx (in HEX)
	/N	  selects no parity configuration
	/? or /H  displays help screen


NOTES:  - When using the BA option (Base Address), all four digits must
          be specified.

        - This program transmits in the UIOF/Microgrid default serial 
          communication configuration:  9600 baud, 7 data bits, even parity,
          and two stop bits.

        - Use the /BA switch only when the serial port is located at a 
          non-standard address within the computer.

	- A summary of command line switches is always available by starting
          the program with switch /? or /H.


Serial Port Address Table

Command Line	Serial	   Serial Port	 System
Switch		Port	   Address		
------------------------------------------------------------------------------
/1		1	   03F8 Hex	 All (PC, XT, AT, 386, and any PS/2)
/2		2	   02F8 Hex	 All (PC, XT, AT, 386, and any PS/2)
/3		3	   3220 Hex	 Any PS/2
/4		4	   3228 Hex	 Any PS/2
/5		5	   4220 Hex	 Any PS/2
/6		6	   4228 Hex	 Any PS/2
/7		7	   5220 Hex	 Any PS/2
/8		8	   5228 Hex	 Any PS/2
------------------------------------------------------------------------------

*********************** 87-4007-001 ***************************