MONITOR


Rev 1.1
Release Date
September 28,1989



			******** DISCLAIMER ********

The FBUG monitor is the sole property of Motorola Inc. This software may be
distributed in whole or in part as public domain software. This software is 
provided as is and in no event shall Motorola, Inc. be liable for any direct, 
special, incidental, or consequential damages arising out of or connected with
a users poseesion or use of this software package, even if Motorola has advance
notice of the possibility of such damages.

Comments, questions or suggestions may be directed, in writing only, to:

		Microprocessor Products Applications
		6501 William Cannon Drive West 0E33
		Austin, Texas 78735-8598

			*****************************









TABLE OF CONTENTS

1.      GENERAL INFORMATION
1.1     Description of FBUG.......................      3


2.      THE FBUG COMMAND SET
2.1     Introduction..............................      4
 2.2     Assembler/Disassembler (as) ..............      6
2.3     Block of Memory Fill (bf).................      6
2.4     Block of Memory Move (bm).................      6
2.5     Break Point (br)..........................      6
2.6     Block Search (bs).........................      7
2.7     Confidence Test (ct)......................      7
2.8     Data Conversion (dc)......................      7
2.9     Go (go)...................................      7
2.10    Help (?/he/help)..........................      8
2.11    Load S-Records (lo).......................      8
2.12    Memory Display (md).......................      8
2.13    Memory Modify (mm)........................      9
2.14    Register Display (rd).....................      10
2.15    Register Modify (rm)......................      10
2.16    Symbol Define (sd)........................      10
2.17    Transparent Mode (tm).....................      10
2.18    Trace (tr)................................      11

3       USING THE ONE-LINE ASSEMBLER/DISASSEMBLER
3.1     Introduction  ............................      12
3.2     Entering and Modifying Source Program ....      12
3.3     Entering a Source Line....................      12
3.4     Entering Branch and Jump Addresses........      14
3.5     Entering Register Lists ..................      15
3.6     Entering Floating Point Immediate Data ...      15
3.7     Entering MMU Instructions ................      15


4       SOFTWARE MODIFICATIONS
4.1     Introduction ............................. 	16
4.2     Adding/Deleting Commands ................. 	16
4.3     Switching Drivers ........................ 	17

5       TARGET SYSTEM CONFIGURATION
5.1     Introduction ............................. 	17
5.2     Assembler/Disassembler ................... 	18
5.3     Memory Requirements ...................... 	18

6	LINKING INFORMATION	
6.1	Introduction .............................	19	
6.2	Description of FBUG (68xxx) Makefile .....	19
6.3	Monitor used to boot the system ..........	19

7	ERROR REPORTING 
7.1	Error Listing .............................	19	

CHAPTER 1
GENERAL INFORMATION


1.1     DESCRIPTION OF FBUG(68xxx)

The FBUG monitor is a stand alone software package designed to assist in
evaluating/debugging systems which use the 68xxx Microprocessor.  It has the
capability to load and execute user code and includes an assembler/disassembler
designed for quick program patchwork.  The monitor operates in a user-
interactive command driven mode signified by the MOTOROLA> prompt.  The
command line entered after this prompt determines which operation is
performed.



CHAPTER 2
THE FBUG COMMAND SET

2.1     INTRODUCTION

This chapter explains the FBUG monitor commands and their associated syntax.
Table 2.1 summarizes the available commands and shows the section where the
command is explained in greater detail. 

                        TABLE 2.1  FBUG MONITOR COMMANDS

Command Mnemonic        Name                    Section


        as      Assembler/Disassembler          2.2
        bf      Block of Memory Fill            2.3
        bm      Block of Memory Move            2.4
        br      Breakpoint                      2.5
        bs      Block of Memory Search          2.6
        ct      Confidence Test                 2.7
        dc      Data Conversion                 2.8
        go      Go                              2.9
 ?/he/help      Help                            2.10
        lo      Load S-Records                  2.11
        md      Memory Display                  2.12
        mm      Memory Modify                   2.13
        rd      Register Display                2.14
        rm      Register Modify                 2.15
        sd      Symbol Define                   2.16
        tm      Transparent Mode                2.17
        tr      Trace                           2.18



The command line is composed of:

        <COMMAND IDENTIFIER>: specifies which command (ex. br )
        <SP>: at least one space
        OPTION LIST: an option delimiter(-) with options if non-default options
                        are allowed and are being used. (ex. [<-r>])
        <SP>: at least one space
        ARGUMENTS: any required arguments specified by the command separated
                        by commas/spaces as shown in the command description.
                        (ex. <ADDR,ADDR>)


where "<>" enclose symbols that are required on the command line and "[<>]" 
enclose symbols that are optional on the command line.  Note, in the above 
examples the -r option was an example of an optional symbol and that the ADDR 
fields are requirements on the command line.  The options available with a given
command are fully explained in the section that describes that command.  The 
monitor is not case sensitive to input from the terminal. All input from the 
terminal is converted to lower case before being used internally (except text 
following a text delimiter; See TEXT below).  The arguments of a given command 
are described using the following symbols:


<EXP>: An expression can be any numerical expression which may be
       evaluated using only the arithmetic + and - operators.

                 Ex.     1000
                 Ex.     1+3
                 Ex.     13+/reset   NOTE: where /reset has been
                                           predefined (see section 2.16 )

Note: Numbers may be preceded with a base designator if the default
(hexadecimal) is not desired. These designators are shown below in
Table 2.2:

                        TABLE 2.2  BASE DESIGNATORS

                        _______________________
                        Base         Designator
                        _______________________

                        Hexadecimal     $
                        Decimal         &
                        Octal           @
                        Binary          %

<ADDR>: Address field is any valid expression. Note: This address field should
        not be confused with the source and destination addresses required
        using the Assembler/Disassembler.

<COUNT>: Count field is any valid expression preceded by a COUNTDEL (count
        delimiter ie. ":")

                Ex.     :100

<RANGE>: A range of memory locations denoted by either ADDR,ADDR or ADDR:COUNT.

                Ex.     0,100
                Ex.     0:50


<TEXT>: An ASCII string of up to 255 characters preceded by a TEXTDEL (text
        delimiter ie. ";")

                Ex.     ;sample text

<SIZE>: Can be either:
                byte    (8   bit)       ====> -b
                word    (16  bit)       ====> -w
                long    (32  bit)       ====> -l

                Note: ====> stands for "is represented by" or "returns"

<DATA>: Data can be any valid expression.

<MASK>: A mask may be any expression.  After evaluating the expression 0's
        represent don't cares.  A mask is sometimes used to qualify
        <DATA>. See section 2.6 for an example of usage.


2.2     ASSEMBLER/DISASSEMBLER
        as <ADDR>

The assembler/disassembler is invoked at the address given and disassembles
the object code at that location.  Use of the Assembler/Disassembler is fully
described in chapter 3.


 2.3    BLOCK OF MEMORY FILL
        bf [<SIZE>] <RANGE> <DATA>

The block fill command fills the specified range of memory with the data listed.
If the size option is not specified the default size used is word.  If a 
multiple of the <SIZE> of <DATA> does not fit evenly in the <RANGE> the command 
leaves the last partial word or long word unchanged. 

        Examples of use:

        bf 100,110      &10
        bf 100:8        &10
        bf -w 100:8     a
        bf -l 100,110   a000a

        Note: All of these examples perform the same memory fill.
	      (ie.  $00000100: $000a $000a $000a $000a $000a $000a
	            $0000010C: $000a $000a $0000 $0000 $0000 $0000 )

2.4     BLOCK OF MEMORY MOVE
        bm [<SIZE>] <RANGE> <ADDR>

The block move command allows the user to copy segments of memory to different
locations in memory. The execution of this command does not destroy the original
version unless the location moved to <ADDR> is within the range <RANGE> of the
code being copied.  The size option is only available when range is described as
<ADDR>:<COUNT> .  If range is being described with the <ADDR>,<ADDR>  mode the
size defaults to byte. The size field represents the size transfer that is used
to accomplish the memory move.


        Examples of use:

        bm 1000,2000    10000
        bm 1000:800     10000
        bm -l 1000:400  10000   Note: This variation executes the fastest

        Note: All of these examples perform the same memory move.

2.5     BREAKPOINT
        br
        br <ADDR>
        br <ADDR> <:COUNT>
        br -r [<ADDR>]
        br -r

The breakpoint command allows the user to list, insert or delete breakpoints in 
the target code. This allows the user to stop executing a program and return to the monitor environment when the specified <ADDR> is prefetched.  The different 
uses of this command are summarized below:

        br                              list all known breakpoints
        br <ADDR>                       insert a breakpoint at this address
        br <ADDR> <:COUNT>              insert a breakpoint at this address
                                        ,however, return to the monitor
                                        environment only after encountering the
                                        breakpoint <COUNT> number of times.
        br -r [<ADDR>]                  remove the breakpoint at this address
        br -r                           remove all breakpoints


2.6     BLOCK SEARCH
        bs [<SIZE>] <RANGE> <DATA>
        bs [<SIZE>] <RANGE> <DATA> <MASK>


The block search command allows the user to find a specific pattern within 
memory.  The search area may extend beyond the <RANGE> specified if a pattern is
started within <RANGE>.  There are two primary types of searches:

        bs [<SIZE>] <RANGE> <DATA>              searches the range for an
                                                exact match of <DATA>.
        bs [<SIZE>] <RANGE> <DATA> <MASK>       searches the range for any
                                                pattern that matches <DATA>
                                                where there is a "1" in the
                                                binary representation of
                                                the mask.

	Ex. With memory at location $100 as shown below, executing
	    "bs 100,118 $1234 $ffbf" ====>

		Starting address: $00000100
		Ending   address: $00000117
		Found at: $00000110:$1234
		Found at: $00000114:$1274


		Memory for the example above:

            $00000100: $0000 $0000 $0000 $0000 $0000 $0000
            $0000010C: $0000 $0000 $1234 $0000 $1274 $0000


2.7     CONFIDENCE TEST
        ct

The confidence test command allows the user to perform a confidence test of the 
system being evaluated. This command is designed to write a -1 into the result 
variable (int confres in vardef.h) of the confidence test and then pass the 
address of this variable in register a0 to a called subroutine. This routine 
writes a 0 or 1 into confres depending on whether the test passes or fails
respectively. If the routine does not place a valid result in this variable
then the monitor assumes that the confidence test was not performed and displays
"ERROR 14:Unable to perform Confidence Test".  The confidence test to be
performed is system dependent and has to developed for the system on
which the monitor is running.


2.8     DATA CONVERSION
        dc <EXP>

The data conversion command allows the user to evaluate an input expression and 
determine its hexadecimal and decimal equivalent.

        Examples of use:

        NOTE:   The following symbols have been defined earlier in order
		fpr them to be used in the examples below:
		EX 1.   uses	/start= 0           
                Ex 2.   uses	/start= - $18
                Ex 3.   uses	/finish= 10000 and /start=$10000
		(see section 2.17 )

        Ex. 1   dc $17+/start      ====>   $17 = &23
        Ex. 2   dc $17+/start      ====>   UNSIGNED  :  $FFFFFFFF = &4294967295
                                      	   SIGNED    :        -$1 = -&1
        Ex. 3   dc $/finish-/start ====>   $10000 = 65536


2.9     GO
        go [<ADDR>]

The go command allows the user to execute target programs. If an address is not
specified on the command line then the current PC value is used.This value is 
either 1.)the initialized PC value if no target code has been run,2.)the last
value of the PC used in executing target code or 3.)the value placed into the PC
register by a RM command (Register Modify see section 2.16 ). If an address is 
included on the command line then the PC is modified to be the specified addr. 
and execution begins at this address.  In both cases, the register state that 
the microprocessor is intialized to, before executing the target code at this
location, can be viewed by executing a rd command (See section 2.15).


2.10    HELP
        ?    [<symbol>]
	he   [<symbol>]
        help [<symbol>] 

The help command allows the user to view a list of allowable commands and the
syntax associated with them.  Symbols used to describe the command usage can be 
looked up also.

        Examples of use:

        ?,he or help ====>  return a complete listing of all commands with usage
        ? as         ====>  AS <addr>
        help addr    ====>  <number>
        he number    ====>  <hex> || <dec> || <oct> || <bin> || <symbol>

                Note: <number> may also be an expression

2.11    LOAD S-RECORD
        lo [<OFFSET>] ;<TEXT>

The load command allows the user to download S-Records from the host system.  If
an offset is present on the command line then the target address is the offset 
added to the address determined by the S-Record. This command sends the <TEXT> 
beyond the ";" to the HOST.  It then expects the HOST to begin sending S-Records
to the terminal.

        Examples of use:

        lo ;cat fbug.mx

Note:   The "cat" command is a UNIX command that concatenates and then prints
        the specified files using standard output. This effectively sends 
	the contents of the file to the terminal. The monitor then loads the
	contents of the S-Records in the file to the addresses determined by 
	the S-Records.

        lo a0000 ;cat fbug.mx

                Note: 	This command downloads the same S-Record file used
			in the first example except that it is down loaded 
			into memory at the address determined by the 
			S-Record + $a0000 (ie. the offset is added in).

2.12    MEMORY DISPLAY
        md [<SIZE>]  <addr>
        md [<SIZE>]  <RANGE>
        md -di <addr>

The memory display command allows the user to view memory.  The size used to dis
play the memory is determined by the size option.  If no option is used the 
default is word.  If the range exceeds the screen capacity, output to the screen
is suspended until any key is pressed.

        Examples of use:

        md -l 100,110
        md -l 100:4
        md 100:8
        md -di 100	Note: This command begins to disassemble the memory at
			      this location.



2.13    MEMORY MODIFY
        mm [<SIZE>]  <ADDR>
        mm <CONTROL>

The memroy modify command allows the user to view and modify memory.  The size 
used to display the memory is determined by the size option.  The size default 
is word.  Memory is displayed beginning at the address specified followed by a 
'?' prompt.  The user may type in an <exp> to replace that memory value or hit 
return to view the next memory value.  To exit the command, type ". <cr>" 
(period <carriage return>).  Other available <CONTROL> characters are summarized
below in Table 2.3:

                        TABLE 2.3  CONTROL CHARACTERS

                        __________________________________
                        Control Character       Designator
                        __________________________________

                        - <EXP>                 backup  <EXP> memory locations
                        + <EXP>                 advance   "     " 	"

        Examples of use:

        mm -l 100 ====> $00000100 $00000000 ?
        mm 100    ====> $00000100 $0000 ?        
		(ie. uses the default "word" size)



2.14    REGISTER DISPLAY
        rd
        rd -f   Note: Only valid if Coprocessor support has been specified
		      see below.

The register display command allows the user to view the contents of the 
registers of the mpu/fpu.  Versions released before August 30,1989 only 
supported the 68020 programmers model and did not support the coprocessor 
(68881/882) programmers model.  Versions released after August 30,1989 support 
the programmers model that the user specifies before compiling the monitor.  
This is done by using the DEVICE,EMULATOR and COPROCESSOR "define" statements in
the "targetsys.h" header file. These defines are discussed further in the 
"Target System Configuration" section. The values shown for the registers are 
either 1.) the initialized register state if no target code has been run, 2.) 
the last values in the registers  while executing target code or 3.) the values 
specifically placed into the registers by a rm command.  


2.15    REGISTER MODIFY
        rm [<REGISTER> [<New Value>]]


The RM command allows the user to the modify the contents of the registers of 
the mpu. 

        Examples of use:

        To change the PC value:

        rm pc 3000      ====>   changes the PC value to 3000

                or

        rm              ====>   Which register?
        pc              ====>   PC=00004000NEW VALUE?
        3000            ====>   changes the PC value to 3000

                or

        rm pc           ====>   PC=00004000NEW VALUE?
        3000            ====>   changes the PC value to 3000




2.16    SYMBOL DEFINE
        sd [<SYMBOL>  <EXP>]
        sd -r <SYMBOL>


The symbol define command allows the user to define symbols.  These symbols can 
then be used within expressions. Using a symbol in an expresion results in the 
symbol being substituted with the expresion that was used to define it.  Once 
defined, the symbol is available until the monitor is reset.  If a symbol is 
defined multiple times the monitor uses the first definition.


        Examples of use:

        sd              ====>   lists which symbols are already
                                known
        sd /reset 10000 ====>   defines /reset to be $10000
                                whenever it is used in an expression.
        sd /start -$18  ====>   defines /start to be -$18
                                whenever it is used in an expression.
        sd -r /start    ====>   removes the first definition of /start
                                from the list

        NOTE:   Symbols that have been defined using the sd command can
                be used in any expressions. An example of this is to
                use a symbol defined to enter source code while in
                the assembler (ie.  bsr    /startsub     after defining
                /startsub).

2.17    TRANSPARENT MODE
        tm

The transparent mode command places the user into transparent mode by 
establishing a software connection between the HOST and TERMINAL.  Transparent 
mode preempts normal communication between the TERMINAL and the debugger. While 
in this mode all keyboard input is relayed directly to the HOST. HOST responses,
in turn, are returned to the screen. Typing a CTRL A returns the user to the 
monitor environment.


2.18    TRACE
        tr [<ADDR>][<COUNT>]

The trace command allows the user to trace though target code and observe the 
registers after executing the command line.  If count is specified then the 
microprocessor executes <COUNT> number of instructions before returning to the 
monitor environment.  Trace begins from the <ADDR> listed on the command line or
from the current PC if an <ADDR> is not included.  The trace instruction can be
continued by hitting a carriage return.  To exit, a "." must be entered.

        Examples of use:

        tr              ====>  traces 1 instruction from the current PC
        tr :10          ====>  executes 10 instructions past the current
                                  PC then returns to the monitor
                                  environment
        tr 1000         ====>  traces 1 instruction starting at $1000




CHAPTER 3
USING THE ONE-LINE ASSEMBLER/DISASSEMBLER


3.1     INTRODUCTION

Included in the FBUG monitor is an assembler/disassembler command which can
be executed as detailed in the previous chapter.  This assembler/disassembler
allows the user to modify target code.  Each source line that is typed in by the
user is entered into memory at the displayed address.  This line is then
disassembled so that the user can verify the actual code entered into memory. If
no change is desired a <CR> moves the user to the next opcode in memory.

NOTE:   The instruction set that is available to the user is determined when
	the monitor is compiled. The choice of the values of DEVICE, EMULATOR
	and COPROCESSOR determine which instruction set is available.
	See the "Target System Configuration" section below.

CAUTION:  This assembler/disassembler does not insert code into the source
          program; it merely overwrites memory at that location.  As a
          result, a program patch that requires code insertion can be
          accomplished by first Block Moving code to free up an insertion
          area and then inserting into that area.

3.2     ENTERING AND MODIFYING SOURCE PROGRAM

In order to enter and modify source code, the as command should be executed as
detailed in section 2.2 (ie. as <ADDR>).  This places the user into the
Assembler/Disassembler routine.  Table 3.1 summarizes the commands that can
be executed within this routine:

                TABLE 3.1  ASSEMBLER/DISASSEMBLER SUB COMMANDS

                        __________________________________
                        Command                 Designator
                        __________________________________

                        BACKUP <EXP>                    - <EXP>
                        ADVANCE <EXP>                   + <EXP>
                        FINISH                          .
                        HELP                            ?
                        STEP PAST               carriage return
			DEFINE CONSTANT		    DC #<EXP>

Note: Executing a '?' while in the assembler/disassembler returns the DEVICE
      that the assembler/disassembler is supporting.

3.3     ENTERING A SOURCE LINE

After executing an as <ADDR> command, the assembler/disassembler 
returns with the disassembly of the code found at that location.  At this
time the user may execute an assembler command shown in section 3.2 or type in
the source line that is to replace the displayed source code.  While entering
source the standard MOTOROLA effective addressing modes are used.  These modes
are summarized below in Table 3.2:



TABLE 3.2  ASSEMBLER/DISASSEMBLER EFFECTIVE ADDRESSING MODES



Effective Addressing Mode                               Syntax


Register Direct                                 Dn
Address register direct                         An
Address register indirect                       (An)
Address register indirect
          with Postincrement                    (An)+
Address register indirect
          with Predecrement                     -(An)
Address register indirect
          with Displacement                     (d16,An)
Address register indirect
          with Index (d8)                       (d8,An,Xn.SIZE*SCALE)
Address register indirect
          with Index (base displacement)        (bd,An,Xn.SIZE*SCALE)
Memory indirect Post-indexed                    ([bd,An],Xn.SIZE*SCALE,od)
Memory indirect Pre-indexed                     ([bd,An,Xn.SIZE*SCALE],od)
PC indirect with displacement                   (d16,PC)
PC indirect with index (d8)                     (d8,PC,Xn.SIZE*SCALE)
PC indirect with index (bd)                     (bd,PC,Xn.SIZE*SCALE)
PC memory indirect Post-indexed                 ([bd,PC],Xn.SIZE*SCALE,od)
PC memory indirect Pre-indexed                  ([bd,PC,Xn.SIZE*SCALE],od)
Absolute Short Address                          (xxx).W
Absolute Long Address                           (xxx).L
Absolute Address                                xxx optimizes (bwl)
Immediate Data                                  #xxx



While using the POST or PRE indexed modes, fields may be skipped by using a
comma.  An example is shown below:

        Ex.     andi #12,([,],,)                ====>
                                andi.b #$12,([$0,ZA0],ZD0.W*1,$0)

Other examples of source lines are shown below:

        Ex.     ori.l  #12,(a1)                 =====>  ori.l #$12,(a1)

        Ex.     addq    #1,(a1)                 =====>  addq.b #$1,(a1)

There are only limited error screening abilities included within the monitor.
Examples of this are shown below:

        Ex.     jmp (123).w                     ====>   jmp ($123).W

                        Note: 	When executed results in a bus error.

		
	Ex. 	bsr (123) ====> 

	ERROR 10:illegal change of flow ===> bsr (123)

			Note: 	The bsr instruction does check for illegal 
			      	changes of flow.  

	NOTE:	Flow may not be changed to an odd addr.

Upper digits of data are NOT truncated when a mismatch between size and 
immediate data is found if the byte or word size option was specifically 
entered. If the long size option is specified and data exceeds this range then 
upper digits ARE truncated.

	Ex.	addi.b #12345678,(a1) ====> 

	ERROR 11:immediate data/size option error ===> addi.b #12345678,(a1)

	Ex.	addi.l #123456789,(a1) ====>  addi.l #$23456789,(a1)
	Ex.	addi   #123456789,(a1) ====>  addi.l #$23456789,(a1)
			(defaults to the long option)
				truncated--------------^

Upper digits of data are truncated on commands that have a limited field
in the opword to store the immediate data. Examples of this are shown below.

        Ex.     addq    #10,(d0)        =====>  addq.b #$0,(d0)

        Ex.     trap    #10             =====>  trap #$0   input is hex default

        Ex.     trap    #&10            =====>  trap #$A



3.4     ENTERING CHANGE OF FLOW INSTRUCTIONS

Since the assembler/disassembler does not use labels, all instructions that use
<label> as an effective addressing mode must have their displacement determined.
If initially unknown,  space for this displacement must be reserved and then the
user needs to come back and enter the displacement.  Once the displacement
has been determined it may be entered as shown in the following example:

Ex. In this example the location of the target instruction of a branch is known
to be $100000 and a BRA is needed at location 0.  After executing "AS 0" and 
obtaining the disassembly found at 0 the user could type:

                BRA     100000          or
                BRA     (100000)        or
                BRA.l   #ffffe

The absolute addressing mode can be used if the target address of a branch is
known (as in the first 2 examples) or the displacement (last example) can be 
entered using the immediate data addressing mode. 


CAUTION:  	In some instances unexpected results can occur while using 
		change of flow statements.  These instances are summarized below
		with examples.

Ex. 1  If the degenerate case of a branch statement in used (ie. attempting to
use a short branch to branch to the following instruction) the assembler 
mistakenly assembles this .b option.  However, since the displacement is zero
this is a .w opcode and the disassembler correctly displays this fact to the
user.

        $00004000       nop  ? bra.b  ====> results in an INCORRECT assembly

Ex. 2  If the user attempts to force a particular size branch statement and the
actual branch requires a greater displacement than was reserved then the
assembler prints an error message: "ERR0R 16:  OUT OF DISPLACEMENT RANGE" .

        $00004000       nop  ?bra.w (100000)

One way to assure this does not occur is to not enter a size option.  This 
allows the assembler to choose the correct size for the displacement.



3.5 ENTERING REGISTERS and REGISTER LISTS

The move multiple register instruction (movem) uses a register list as an 
effective address.  This list may be entered in the following method:

	Ex.

        a0                      ====>   single address register
        d3                      ====>   single data register
        a0-a3                   ====>   series of registers
        a0-a3/a7                ====>   combination of previous examples
        a0-a7/d0-d7             ====>   all of the registers

	If coprocessor support is specified  then the floating point registers
	can be entered as shown below: 

	Ex.

        fp0                      ====>   single floating point register
        fp0-fp2                  ====>   series of registers
        fp0-fp3/fp7              ====>   combination of previous examples

Many of the commands require the entering of registers other than data or
address registers.  Tables 3.3-8 show listings of the registers that are used
and the abbreviations accepted by the assembler:

                        TABLE 3.3  68000/68HC000/68008 REGISTERS

                ____________________________________________
                Name                                    Syntax
                ____________________________________________
                User Stack Pointer                      USP
                Program Counter                         PC
                Condition Code Register                 CCR
                Supervisor Stack Pointer                SSP
                Status Register                         SR

                        TABLE 3.4  68010 REGISTERS

                ____________________________________________
                Name                                    Syntax
                ____________________________________________
                User Stack Pointer                      USP
                Program Counter                         PC
                Condition Code Register                 CCR
                Supervisor Stack Pointer                SSP
                Status Register                         SR
                *Vector Break Register                  VBR
                *Source Function Code Register          SFC
                *Destination Function Code Register     DFC

		Note: * Represents a change from the previous
			model

                        TABLE 3.5  68020 REGISTERS

                ____________________________________________
                Name                                    Syntax
                ____________________________________________
                User Stack Pointer                      USP
                Status Register                         SR
                Condition Code Register                 CCR
                Program Counter                         PC
                *Master Stack Pointer                   MSP
                *Interrupt Stack Pointer                ISP
                Vector Break Register                   VBR
                Source Function Code Register           SFC
                Destination Function Code Register      DFC
                *Cache Control Register                 CACR
                *Cache Address Register                 CAAR
                _____________________________________________

                        TABLE 3.6  68030 REGISTERS

                ____________________________________________
                Name                                    Syntax
                ____________________________________________
                User Stack Pointer                      USP
                Status Register                         SR
                Condition Code Register                 CCR
                Program Counter                         PC
                Master Stack Pointer                    MSP
                Interrupt Stack Pointer                 ISP
                Vector Break Register                   VBR
                Source Function Code Register           SFC
                Destination Function Code Register      DFC
                Cache Control Register                  CACR
                Cache Address Register                  CAAR
                *CPU Root Pointer Register              CRP
                *Supervisor Root Pointer Register       SRP
                *Translation Control Register           TC
                *Transparent Translation Register 0     TT0
                *Transparent Translation Register 1     TT1
                *MMU Status Register                    PSR
                _____________________________________________

                        TABLE 3.7  68040 REGISTERS

                ____________________________________________
                Name                                    Syntax
                ____________________________________________
                User Stack Pointer                      USP
                Status Register                         SR
                Condition Code Register                 CCR
                Program Counter                         PC
                Master Stack Pointer                    MSP
                Interrupt Stack Pointer                 ISP
                Vector Break Register                   VBR
                Source Function Code Register           SFC
                Destination Function Code Register      DFC
                Cache Control Register                  CACR
                Cache Address Register                  CAAR
                User Root Pointer Register              URP
                Supervisor Root Pointer Register        SRP
                Translation Control Register            TC
                *Data Transparent Translation Register 0 DTT0
                *Data Transparent Translation Register 1 DTT1
                *Instruction Transparent Trans. Reg.   0 ITT0
                *Instruction Transparent Trans. Reg.   1 ITT1
                MMU Status Register                     PSR
		
		Note: Also the floating point registers below
                _____________________________________________

                        TABLE 3.8  FLOATING POINT REGISTERS

                ____________________________________________
                Name                                    Syntax
                ____________________________________________
                Floating Point Control Register         FPCR
                Floating Point Status Register          FPSR
                Floating Point Inst. Address Register   FPIAR
                Floating Point Data Register            FP0-FP7

NOTE:	PMMU (68851) support is not available under release 1.0.	


3.6 ENTERING/EVALUATING FLOATING POINT IMMEDIATE DATA

Floating point immediate data must be entered using a decimal point with at 
least one (1) digit in front of the decimal place (even if it is a '0'). 
Ex. 0.0012.  Since the C compiler used was not based on the draft proposed 
version of ANSI C the software is incapable of performing the 'assembling' of 
extended immediate data to extended precision. The monitor makes the correct
conversion up to double precision and places this result in an extended 
format.  If the compiler that is being used does conform to allowing a 
'long double' type then changing the type of the variable 'weight' in the 
EAallowed routine (in the asm68.c file) from double to long double should 
provide the added precision.  Examples of floating point immediate data shown
below:

	Ex.  fmove.s #5.0,fp0	====> fmove.s 1_400000_E_2,FP0

The format on the disassembly is integer part_fraction field_E_exponent field,
where the fraction bits represent weighting of 1/2 ,1/4,....etc. from the left
to the right.  The exponent bits represent the unbiased power that 2 should be
raised to. A conversion to decimal can be accomplished by evaluating:

	integer + evaluated fraction  x 2^exponent field

In the above example this equates to:

  	(1 + .25) x 2^2 = 5.0

NOTE:  The monitor uses the round toward zero rounding mode in the assembler 
       when assembling floating point immediate data.

3.7 ENTERING MMU INSTRUCTIONS

MMU instruction should NOT be entered with a size descriptor.  The assembler 
defaults to the correct size.

	Ex. pmove (a0),tt1 	;asssembles

	    pmove.l (a0),tt1 	;does not assemble even though the operation
				;is a long operation. 

A summary of the mnemonic representation of the MMU registers can be found in
Table 3.5 and 3.6 for the 68030 and 68040 monitors respectively.

CHAPTER 4
SOFTWARE MODIFICATIONS


4.1     SOFTWARE OVERVIEW


The FBUG monitor uses 4 header files.  These header files are briefly described
below.  

TARGETSYS.H
This file is the header file that is used to configure the monitor to the
target system. All of the predefined variables that are used by the monitor
are found here.  It is accessed when any call to #include "userdef.h" is
made.

USERDEF.H
This is the file that defines all of the structures that are used by 
the monitor.

TEXTDEF.H
This file has all of the strings that are used by the monitor.  It is also
where most of the structures that are used by the monitor are implemented.


VARDEF.H
This file has all of the global variables that are used by the monitor.


The flow of the FBUG monitor is outlined below:

asmstartport.s ===> coldstartport.c ===> main.c ----|
					    ^-------|

The first source file (asmstartport.s) initializes the microprocessor to a 
known state and then branches to the main{} statement in the coldstartport.c 
routine.  The coldstartport.c routine performs all of the initialization for the
monitor before branching to the mainloop{} routine in the main.c file.  The 
mainloop{} routine is a continuous loop used by the monitor.  From this loop 
the various commands of the monitor are called.


4.2     ADDING/DELETING COMMANDS


The process of adding or deleting commands from the monitor is a relatively
simple process.  Adding a command involves making 2 additions to the textdef.h 
header file and then developing/including the command description file with the 
monitor.

The two changes that need to be made to the textdef.h header file are:

1.) include the function name that implements the command as an externally
defined routine. For example the line in the textdef.h file that states

extern trcmd(),pfcmd(),ascmd(),sdcmd(),ctcmd();

accomplishes this for those five commands.


2.) include the command in the f[] structure with the appropriate information.
For an example of how this is done the "ct" command entry is discussed:

The line

{"ct Confidence Test \n",ctcmd,"ct \n"}

includes the ct command in the f[] structure.  The first textstring (ie. ct 
Confidence Test \n) is the string that is used for the command listing print 
out performed when the help or ? commands are executed.  Also, the first word 
of this string is the command name that is searched for when attempting to 
execute this command.  The function name "ctcmd" is the name of the function 
that is executed when this command is used by the monitor.  The last text 
string (ie. ct \n) is the string that describes the type of syntax used with 
this command.

Next, the command description file has to be written and included in the
makefile of the monitor (see CHP6 LINKING INFORMATION for more information 
concerning the linking process). The calling convention for the functions which
perform the command is to pass the function two parameters. These two parameters
are argc and argv.  They are the number of arguments on the command line and the
actual command line respectively.  

Deleting a command is accomplished by following an analogous path. Removing 
the 2 lines that incorporate a command into the monitor and removing the command
from the linking process effectively remove the command from the monitor.


4.3     SWITCHING DRIVERS

The I/O driver used by the monitor in version 1.0 is for a MC68681 DUART. If the
target system uses some other driver, then the following changes needs to
be made:

1.)     The DUART initialization performed in coldstartport.c has to be
        modified to accomplish the same results with the new driver.

2.)     The user definitions associated with the new driver has to be
        updated in the targetsys.h file.  (ie. the offsets to the various 
	buffers of the new driver)

3.)     It may be necessary to modify the getch and putch routines found in
        getline.c and print.c respectively.



CHAPTER 5
TARGET SYSTEM CONFIGURATION 

5.1 INTRODUCTION

The FBUG monitor can be configured to support any of the 68xxx microprocessors.
This is accomplished by a series of define statements found within the 
"targetsys.h" header file.  By defining which configuration is supported 
additional software can be excluded from the code at compilation time to 
result in a smaller monitor. These space savings are generally accomplished 
based on the size of the assembler/disassembler for the associated 
configuration.  The monitor can also be configured to a specific memory 
configuration.  


5.2   ASSEMBLER/DISASSEMBLER

The assembler/disassembler supported in the 'AS' command is determined by the 
definiton of the DEVICE, EMULATOR and COPROCESSOR variables found in the 
targetsys.h header file. The choices for DEVICE are 68000,68008,68010,68020,
68030 or 68040. This also determines the programmer's model that is supported in
the 'RD' and 'RM' commands. If the DEVICE selected is '68040' then the EMULATOR
define is used to determine whether 68881/68882 commands not implemented in 
hardware should be supported. Placing a 'TRUE' here stipulates that all 
68881/882 instructions should be supported. If there is no software emulation of
these commands then a 'FALSE' should be placed here. If the DEVICE selected is 
either 68020 or 68030 then the COPROCESSOR (TRUE or FALSE) define statement 
determines whether the 68881/882 instruction set should be supported.

Note: As of release 1.0 the 68040 register model is visible but supervisor
      registers other than those implemented on the 68020 are not supported.
      As a result of this the monitor displays the entire 68040 register set 
      and APPEARS to allow the user to modify these registers with a RM command.
      However, when executing target code (GO or TR command) the monitor does
      NOT use these values to intialize the state of the microprocessor
      before executing the target code.  In addition, these registers are NOT
      captured by the monitor if they have been modified by target code. 


5.3	MEMORY REQUIREMENTS 

The "targetsys.h" file contains all of the variables that determine the 
target system configuration.  These variables are listed below and 
needs to be changed to reflect the configuration of the target 
system.

/* ******************************************************************** */
/* ********************** MEMORY MAP FOR DEBUGGER ********************* */

#define DUARTALOC 0xffe02000	/* MC68681 duart channel a */
#define DUARTBLOC 0xffe02008	/* MC68681 duart channel b */

#define ROMLOC 0x100000		/* system ROM space			*/
				/* .text segment should be loaded here	*/
				/* .data segment should be loaded here	*/

#define SYSRAMLOC  0x000fe000	
				/* system RAM space 			*/
				/* NOTE: space must be reserved for the
					 location of the .bss used by
					 the monitor.			*/
				/* Provided the .bss is not larger than
				   1000 (ie. VBRLOC resides at SYSRAMLOC 
				   + 1000) placing the .bss from the 
				   monitor at this location is allowed 	*/

#define ISPLOC SYSRAMLOC+0x2000 /* defines for monitor 	*/
#define MSPLOC SYSRAMLOC+0x1c00
#define USPLOC SYSRAMLOC+0x1b00
#define VBRLOC SYSRAMLOC+0x1000

#define USERPCLOC 0x4000 	/* defines for usercode	*/
#define USERVBRLOC 0x0

/* *********************************************************************** */
#if(DEVICE<68020)
#define USERSSPLOC USERVBRLOC+0x2000	/* Note: Only one of these is
						 used based on the device
						 being implemented */
#else
#define USERISPLOC USERVBRLOC+0x2000
#endif
/* *********************************************************************** */

#define USERMSPLOC USERVBRLOC+0x1c00
#define USERUSPLOC USERVBRLOC+0x1b00

#define SRSTART 0x2700		/* status register	*/

******************************************************************************


The DUART assumed is a MC68681 and its respective channels are found 
at the stated locations.  If this is not the case, then the initialization 
routine in coldstartport.c has to be changed.  

The next 5 locations describe the memory map of the system used for the port. 

The next location describes the value that is placed in the VBR register.

NOTE: 	This is the location of the vector offset table. This space is used
	by the monitor to set up the offset table. 

The next 5 locations describe the initial values that the monitor 
uses for "user code". 

The next location describes the value that is placed in the user's VBR 
register.

NOTE: This is the location of the user's vector offset table and is
      also initialized by the monitor.

SRSTART is the initialized value of the  MC68xxx Status Register 


CHAPTER 6
LINKING INFORMATION 

6.1 INTRODUCTION

The FBUG monitor is a stand alone software package written in C 
and developed under the UNIX environment.  The combined .text and .data  
section of the object file varies from approx. 54K to 87  bytes of memory. 
Different configurations are summarized below in Table 6.1.  The purpose of this
chapter is to describe the method to compile and link the various files that 
make up the FBUG monitor.  There is also a brief description of the necessary 
changes that need to be made in order to port the FBUG monitor to a MC68xxx 
based board.  

                 TABLE 3.3  68000/68HC000/68008/68010 REGISTERS

                ____________________________________________
		DEVICE	COPROCESSOR	EMULATOR	SIZE (KB)
                ____________________________________________
	68000/008/010	----NA-----	---NA---	54K	
		68020	      FALSE	---NA---	61K
		68020	       TRUE	---NA---	81K
		68030	      FALSE	---NA---	65K
		68030	       TRUE	---NA---	87K
		68040	----NA-----	   FALSE	82K
		68040	----NA-----	    TRUE	84K

	NOTE: 	----NA---- represents a don't care
		for that particular DEVICE.

                ____________________________________________


6.2	DESCRIPTION OF FBUG(68xxx) MAKEFILE

The makefile used to create the FBUG monitor under the UNIX 
operating system is shown below and can be found in the file named 
"makefile" in this directory.

MAKEFILE

portbug : coldport.o main.o printport.o getlineport.o general.o \
	asmprocport.o \
	bf.o bm.o br.o bs.o dc.o he.o lo.o rd.o rm.o tm.o \
	mm.o md.o go.o tr.o sd.o as.o asm68.o disasm68.o asmcode68.o \
	asmhandler.o handler.o  asmstartport.o conf.o fproutines.o 68def.o 
	ld ./ifilemb  asmstartport.o asmhandler.o coldport.o \
	printport.o getlineport.o general.o asmprocport.o main.o bf.o bm.o \
	bs.o dc.o he.o lo.o rd.o rm.o tm.o mm.o md.o go.o tr.o br.o \
	sd.o as.o disasm68.o asm68.o asmcode68.o handler.o conf.o \
	fproutines.o  68def.o \
	-m -o fbugxxxd >memmap
	ubuilds fbugxxxd

!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!
NOTE: In fbugxxxd     xxx ===> 000,008,010,020 etc...
			d ===> T or F for whether Coprocessor supported
!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!

main.o :	main.c userdef.h textdef.h vardef.h
	:
	:
	:
	:
	:
asmproc.o : asmproc.c userdef.h textdef.h vardef.h

asmstartport.o : textdef.h vardef.h userdef.h targetsys.h
		/lib/cpp asmstartport.s  > temp.s
		as  -o asmstartport.o temp.s
		rm temp.s
asmcode68.o : textdef.h vardef.h userdef.h targetsys.h
		/lib/cpp asmcode68.s  > temp.s
		as  -o asmcode68.o temp.s
		rm temp.s
asmhandler.o : textdef.h vardef.h userdef.h targetsys.h
		/lib/cpp asmhandler.s  > temp.s
		as  -o asmhandler.o temp.s
		rm temp.s

!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!
	NOTE: 	In order to ease the porting of the monitor to a 
		specific system, a C preprocessor is executed on the 
		three (3) .s files above.  This performs a text 
		substitution into these files from the targetsys.h
		header file.  If the development system being used does
		not support this capability then these text substitutions
		must be made manually.
!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!

Executing the "make" command under UNIX with this makefile 
produces the file "fbug.mx" which is the stand alone monitor.  
The make command performs the following actions:

1.	Checks to see if all of the current .o files on which 
fbugxxxd depends are current.  If not then compile the 
source files to create those object files.  It also checks 
to verify that the files on which these files depend on
are up to date.  If they are not then they are 
compiled first.


/* ******************************!!!!!!!!!********************************* */
NOTE: These dependencies are not conclusive and if a change is made to any of
      the header files then all of the files should be recompiled until
      a thorough understanding of the interdependencies between the modules
      is achieved.

/* ******************************!!!!!!!!!********************************* */
 

2.	After all the required .o files have been brought up to 
date they are linked together in the order described 
after the "ld" command.  The "ifilemb" file is used as a ld 
directive to describe the memory configuration of the 
target system.  In this instance, the target system has 
the following memory configuration:

	00000000-00000255	RAM
	000FE000-00100000	RAM
	00100000-00110000	ROM

	The ifilemb informs the UNIX linker of this target 
configuration and also where to place each section.  In 
this instance the .text section is being placed into ROM 
and the .data and .bss section are being placed in RAM.  
Refer to the "ifilemb" file in this directory.

/* ******************************!!!!!!!!!********************************* */
NOTE: Space has to be made available for both the monitor's vector offset 
      table and the user's vector offset table. (ie. 256 32-bit words has 
      to be available at locations VBRLOC and USERVBRLOC. 
      (ie.  00000000-00000255	RAM)
NOTE: The monitor uses approx. $1000Kb ram for the .bss variables (placed
      at SYSRAMLOC). Next the vector offset table is placed at SYSRAMLOC +
      $1000. Then the stack space used by the monitor is placed above this.
      Using the default configuration provided requires that approx. $2500 
      bytes of RAM be reserved for the monitor begining at location SYSRAMLOC
      and that 256 32-Bit words be reserved at the USERVBRLOC (which
      is at location 0 in the released version).  If user code is run then 
      the user is responsible for making sure that the stack space used by 
      the user does not interfer with the monitors space.
/* ******************************!!!!!!!!!********************************* */

3.	These files are now linked and this file is labeled "fbugxxxd"

4.	Next, the "ubuilds fbugxxxd" command creates an S-Record 
from the fbug file that was previously created.  This S-
Record can be used to download to systems that have the 
capability to load S-Records.
	

The environment that is being worked under has to be able to perform the 
functions stated above in order for the user to create their FBUG object file.


6.3	MONITOR USED TO BOOT THE SYSTEM

If it is desired for the monitor to be at the reset location (ie. logical 
0 in memory)  then the following two lines should be added above 
the start: routine in the asmstartport.s file:

INITSP:	long 0x100000
INITPC	long start

NOTE:  The ifilemb directive must still accurately reflect the 
location of ROM on the system.